## Slide 2
Joystick on Board?
Import Libraries
A
Power-Up
  Import Libraries
  Instantiate Devices and Font
  Display Splash Screen
Start
Set Has_Joystick
Parameter
Instantiate Devices and Load Font
Display Welcome Screen and Tones
OpenSans-9.bdf
thermal_cam_splash.bmp
Yes
No

## Slide 3
Define Sensor Min/Max Temperature Range
B
Define Globally-Used Parameters
Define Default Min/Max Range and Alarm Threshold Values
Define Display and Parameter Colors
thermal_cam_config.py
A
Define Display and Element Size

## Slide 4
Define
element_grid
Helper
Define Helpers
Define
flash_status_message Helper
Define update_histo_frame Helper
B
Define update_image_frame Helper
C
Define
setup_mode
Helper
Define
move_buttons
Helper

## Slide 5
Create Background Color Fill Layer
image_group[0]
Define Display Group
Define Thermal Image Layers
image_group[1:64]
C
Define Value and Label Layers
Image_group[65:77]
D

## Slide 6
Set Display to:
  - Image Mode
  - Active Mode
  - Default Range
Primary Process Setup
Activate Display Group and Play Welcome Tone
D
E

## Slide 7
Hold Display?
Get Camera Data
Display Image?
Update Image Frame (helper)
Update Histogram Frame (helper)
F
Primary Process
Get Camera Data
Display Image or Histogram
Check for Alarm
Alarm Level?
Play Alarm Sound and Flash Pixels
G
F
From End of
Primary Process Loop
Yes
No
No
Yes
No
Yes

## Slide 8
Hold Button Pressed?
Toggle Display_Hold Parameter
Image Button Pressed?
Toggle Display_Image Parameter
G
Focus Button Pressed?
Toggle Display_Focus Parameter
Setup Button Pressed?
Setup Mode (helper)
F
Set or Restore Range Values
Primary Process Loop
Watch Push Buttons
Setup Mode
To Start of
Primary Process Loop
Yes
No
Yes
No
Yes
No
Yes
No

## Slide 10
Clear Minimum, Maximum, and Sum
Clear Histogram Legend
Update Image Frame Helper
update_image_frame
Helper
All Data Processed?
Step Through Camera Data Array
No
Yes
Return Minimum, Maximum, and Sum
Limit Sensor Temperature Value to Default Range
Determine New Min/Max and Sum Values
Assign Color Based on Value
and Update Display

## Slide 11
Clear Minimum, Maximum, and Sum
Display Histogram Legend
Update Histogram Frame Helper
update_histo_frame
Helper
All Data Processed?
Step Through Camera Data Array
No
Yes
Limit Sensor Temperature Value to Default Range
Determine New Min/Max and Sum Values
Count Value Occurrence in Histogram Distribution List
Return Minimum, Maximum, and Sum
Display Histogram Distribution

## Slide 12
Flash SET Status and
Clear Average Label/Value Display
Setup Mode Helper
setup_mode
Helper
Select Button Pressed?
Select Parameter to Change
No
Yes
Return New Minimum, Maximum, and Sum
Set New Parameter Value
Setup Button Pressed?
Yes
No
Display Maximum and Minimum Display Range
Flash RESUME Status and Restore Average Label/Value Display